## Slide 1: UKOPA Dent Management Strategy TooL
25/03/2015
PIWG 15 010

## Slide 2: Dent Management Strategy
Set of rule allow priority ranking for repair based on cond.
Flow chart basis for
Spreadsheet tool
assigned
Based on DMS from document UKOPA/14/016
Tool to assess dents following ILI

## Slide 3: Spreadsheet tool
The program run using command
button on spreadsheet
Blank Spreadsheet looks like this
How the tool is constructed and operated
Spreadsheet shows column
Headers for data which will be filled

## Slide 4: Data Input
Data entered in sequential order
Check data button will help avoid mistakes

## Slide 5: Main Program – Flow Chart Algorithm
Main part of program
Based on flow chart
from document
Questions relating to assessment
Repair/Investigation
Priority is set

## Slide 6: Flow Chart Selections
Use Y/N controls to
Select correct data
Follow chart through
Lines will shade progress
Press re-enter data button
to correct mistakes
Certain questions require
More than Y/N answer
e.g. weld type

## Slide 7: Flow Chart Selections
Dent depth and strain
Associated Corrosion Depth
Once questions complete, priority is indicated in red
Save Data to
Spreadsheet

## Slide 8: FATIGUE ANALYSIS
Certain set of choices end in the requirement of a
Dent fatigue analysis
Run by clicking control button
Enter cycle data
In sequential order
If dent has assoc.
Corrosion then a
Corrosion length +
Width will be
requested

## Slide 9: FATIGUE ANALYSIS
Fatigue Life screened
Against EPRG Fatigue model
Conservative fatigue life
If fatigue life exceeded
A dent SCF is calculated and
Class B S-N curve from BS 7608
Used for more realistic fatigue life

## Slide 10: DATA OUTPUT
Pipeline data and dent data
Columns filled based on input
Questions from flow chart
Shown as shaded Y/N or N/A
If answer not required
Last 2 columns give priority
Rating. A number is given and
A data bar showing a
Visual representation